## Slide 1: Ch. 2 : Preprocessing of audio signals in time and frequency domain
Time framing
Frequency model
Fourier transform
Spectrogram

## Slide 2: Revision: Raw data and PCM
Human listening range 20Hz  20K Hz
CD Hi-Fi quality music: 44.1KHz (sampling) 16bit
People can understand human speech sampled at 5KHz or less, e.g. Telephone quality speech can be sampled at 8KHz using 8-bit data.
Speech recognition systems normally use: 10~16KHz,12~16 bit.

## Slide 3: Concept: Human perceives data in blocks
We see 24 still pictures in one second, then
we can build up the motion perception in our brain.
It is likewise for speech
Source: http://antoniopo.files.wordpress.com/2011/03/eadweard_muybridge_horse.jpg?w=733&h=538

## Slide 4: Time framing
Since our ear cannot response to very fast change of speech data content, we normally cut the speech data into frames before analysis. (similar to watch fast changing still pictures to perceive motion )
Frame size is 10~30ms (1ms=10-3 seconds)
Frames can be overlapped, normally the overlapping region ranges from 0 to 75% of the frame size .
Time framing Video demo: https://youtu.be/lOu-c2UHU00

## Slide 5: Frame blocking and Windowing
To choose the frame size (N samples )and adjacent frames separated by m samples.
I.e.. a 16KHz sampling signal, a 10ms window has N=160 samples, (non-overlap samples) m=40 samples
l=1 (first window), length = N
m
N
N
l=2 (second window), length = N
n
sn
time

## Slide 6: Tutorial for frame blocking
A signal is sampled at 12KHz, the frame size is chosen to be 20ms and adjacent frames are separated by 5ms. Calculate N and m and draw the frame blocking diagram.(ans: N=240, m=60.)
Repeat above when adjacent frames do not overlap.(ans: N=240, m=240.)

## Slide 7: Class exercise 2.1
For a 22-KHz/16 bit sampling speech wave, frame size is 15 ms and frame overlapping period is 40 % of the frame size.
Draw the frame blocking diagram.

## Slide 8: The frequency model
For a frame we can calculate its frequency content by Fourier Transform (FT)
Computationally, you may use Discrete-FT (DFT) or Fast-FT (FFT) algorithms. FFT is popular because it is more efficient.
FFT algorithms can be found in most numerical method textbooks/web pages.
E.g. http://en.wikipedia.org/wiki/Fast_Fourier_transform

## Slide 9: A time domain signal of N samples
Sk=0
Sk=2
S=
Signal
level
Time k
Sk=1
k=0 1 2….
k=N-1

## Slide 10: The Fourier Transform FT method (see appendix of why mN/2)
Forward Transform (FT) of N sample data points
Demo Matlab code: demo_dft_tutorial.rar

## Slide 11: Fourier Transform
Called spectral envelop
S0,S1,S2,S3. … SN-1
Time
Signal
voltage/
pressure
level
Fourier Transform
freq. (m)
single freq..
Power=|Xm|= (real2+imginary2)
Demo Matlab code: demo_dft_tutorial.rar
Demo Video

## Slide 12: Example
[s0,s1,s2,…]=[1 ,3 ,4,…], N=128, m=0,…,64
Xm=0=1*e-j(2*pi*0*0/128)+3*e-j(2*pi*1*0/128)+4*e-j(2*pi*2*0/128) +..
Xm=1=1*e-j(2*pi*0*1/128)+3*e-j(2*pi*1*1/128)+4*e-j(2*pi*2*1/128) +..
Xm=2=1*e-j(2*pi*0*2/128)+3*e-j(2*pi*1*2/128)+4*e-j(2*pi*2*2/128) +..

## Slide 13: Examples of FT (Pure wave vs. speech wave)
time(k)
pure cosine has one frequency band
single freq..
|Xm|
sk
complex speech wave
has many different frequency bands
sk
time(k)
FT
freq.. (m)
freq. (m)
single freq..
|Xm|
Spectral envelop
http://math.stackexchange.com/questions/1002/fourier-transform-for-dummies
DFT and Inverse: DFT https://www.mathworks.com/matlabcentral/fileexchange/41228-dft-and-idft/content/Untitled3.m

## Slide 14: Discrete Fourier transform DFT and Inverse Discrete Fourier transform IDFT
https://en.wikipedia.org/wiki/Discrete_Fourier_transform
Matlab code:
https://www.mathworks.com/matlabcentral/fileexchange/41228-dft-and-idft/content/Untitled3.m

## Slide 15: Use of short term Fourier Transform (Fourier Transform of a frame)
Power spectrum envelope is a plot of the energy Vs frequency.
DFT or FFT
Time domain signal
of a frame
Frequency
domain output
amplitude
time
freq..
Energy
Spectral envelop
time domain signal
of a frame
1KHz
2KHz
First formant
Second formant
FFT video demo: https://youtu.be/EuX2uKZSd40

## Slide 16: Class exercise 2.2: Fourier Transform
Write pseudo code (or a C/matlab/octave program segment but not using a library function) to transform a signal in an array.
  Int s[256] into the frequency domain in
  float X[128+1] (real part result) and
  float IX[128+1] (imaginary result).
How to generate a spectrogram?

## Slide 17: The spectrogram: to see the spectral envelope as time moves forward
It is a visualization method (tool) to look at the frequency content of a signal.
Parameter setting: (1)Window size = N=(e.g. 512)= number of time samples for each Fourier Transform processing. (2) non-overlapping sample size D (e.g. 128). (3) frame index is j.
t is an integer, initialize t=0, j=0. X-axis = time, Y-axis = freq.
Step1: FT samples St+j*D to St+512+j*D
Step2: plot FT result (freq v.s. energy) spectral envelope vertically using different gray scale.
Step3: j=j+1
Repeat Step1,2,3 until j*D+t+512 >length of the input signal.

## Slide 18
A specgram
Specgram: The white bands are the formants which represent high energy frequency contents of the speech signal

## Slide 19
Better time. resolution
Better frequency resolution
Freq.
Freq.

## Slide 20
How to generate a spectrogram?

## Slide 21
Procedures to generate a spectrogram (Specgram1)
Window=256-> each frame has 256 samples
Sampling is fs=22050, so maximum frequency is 22050/2=11025 Hz
Nonverlap =window*0.95=256*.95=243 , overlap is small (overlapping =256-243=13 samples)
For each frame (256 samples)
Find the magnitude of Fourier
X_magnitude(m), m=0,1,2, 128
Plot X_magnitude(m)=
Vertically,
-m is the vertical axis
-|X(m)|=X_magnitude(m) is
represented by intensity
Repeat above for all frames
q=1,2,..Q
|X(0)|
|X(i)|
|X(128)|
Frame q=1
Frame q=Q
frame q=2

## Slide 22: Class exercise 2.3: In specgram1
Calculate the
  first sample location and last sample location of the frames q=3 and 7. Note: N=256, m=243
  Answer:
    q=1, frame starts at sample index =?
    q=1, frame ends at sample index =?
    q=2, frame starts at sample index =?
    q=2, frame ends at sample index =?
    q=3, frame starts at sample index =?
    q=3, frame ends at sample index =?
    q=7, frame starts at sample index =?
    q=7, frame ends at sample index =?

## Slide 23: Spectrogram plots of some music sounds sound file is tz1.wav
High
energy
Bands:
Formants
seconds
Matlab Code:
demo_spectrogram_release16.rar

## Slide 24: spectrogram plots of some music sounds
Spectrogram of
Trumpet.wav
Spectrogram of
Violin3.wav
High
energy
Bands:
Formants
Violin has
complex
spectrum
seconds
http://www.cse.cuhk.edu.hk/%7Ekhwong/www2/cmsc5707/tz1.wav
http://www.cse.cuhk.edu.hk/~khwong/www2/cmsc5707/trumpet.wav
http://www.cse.cuhk.edu.hk/%7Ekhwong/www2/cmsc5707/violin3.wav

## Slide 25: Exercise 2.4
Write the procedures for generating a spectrogram from a source signal X.

## Slide 26: Summary
Studied
  Basic digital audio recording systems
  Speech recognition system applications and classifications
  Fourier analysis and spectrogram

## Slide 27: Appendix

## Slide 28: Answer: Class exercise 2.1
For a 22-KHz/16 bit sampling speech wave, frame size is 15 ms and frame overlapping period is 40 % of the frame size. Draw the frame block diagram.
Answer: Number of samples in one frame (N)= 15 ms / (1/22k)
= 15*(10^-3) /(1/(22000))=330
Overlapping samples = 132, m=N-132=198.
Overlapping time = 132 * (1/22k)= 132 * (1/22000) =6ms;
Time in one frame= 330* (1/22k)= 330* (1/22000)=15ms.
l=1 (first window), length = N
m
N
N
l=2 (second window), length = N
n
sn
time

## Slide 29: Answer Class exercise 2.2: Fourier Transform
For (m=0;m<=N/2;m++)
{
  tmp_real=0; tmp_img=0;
  For(k=0;k<=N-1;k++)
  {
    tmp_real=tmp_real+Sk*cos(2*pi*k*m/N);
    tmp_img=tmp_img-Sk*sin(2*pi*k*m/N);
  }
  X_real(m)=tmp_real;
  X_img(m)=tmp_img;
}
From N input data Sk=0,1,2,3..N-1, there will be 2*(N+1) data generated, i.e. X_real(m), X_img(m), m=0,1,2,3..N/2 are generated.
E.g. Sk=S0,S1,..,S511  X_real0,X_real1,..,X_real256, X_imgl0,X_img1,..,X_img256,
Note that X_magnitude(m)= sqrt[X_real(m)2+ X_img(m)2]
http://en.wikipedia.org/wiki/List_of_trigonometric_identities

## Slide 30: Answer: Class exercise 2.3: In specgram1 (updated)
Calculate the
  first sample location and last sample location of the frames q=3 and 7. Note: N=256, m=243
  Answer:
    q=1, frame starts at sample index =0
    q=1, frame ends at sample index =255
    q=2, frame starts at sample index =0+243=243 (so the gap between the q=1 frame and q=2 frame is 243)
    q=2, frame ends at sample index =243+(N-1)=243+255=498 (so q=2 frame has 256 samples)
    q=3, frame starts at sample index =0+243+243=486
    q=3, frame ends at sample index =486+(N-1)=486+255=741
    q=7, frame starts at sample index =243*6=1458
    q=7, frame ends at sample index =1458+(N-1)=1458+255=1713

## Slide 31: Why in Discrete Fourier transform the summation is from k=0 to k=N-1 and m is ranging from 0 to N/2?
Since , Fourier frequency real-value outputs are mirrored around the vertical axis at 0, so using half are fine for calculating the energy during the calculation of the spectrum. It is only an engineering approach to save time. In fact the real definition is using N sample for forward and inverse Fourier transform where all complex numbers are used.
The problem is actual very deep mathematically, ie, how many samples should we use in forward and reverse transform. To get the best result, one should add more zeros to the original sequence (zero padding at the end of the sequence) to increase frequency resolution. x = 1 2 4 6 5 4 3 >> fft(x), Columns 1 through 4 25.0000 + 0.0000i -7.5734 + 0.3479i -0.4620 + 1.7568i -0.9647 - 0.5410i -0.9647 + 0.5410i -0.4620 - 1.7568i -7.5734 - 0.3479i
Antilasing Demo: https://www.youtube.com/watch?v=ByTsISFXUoY
https://www.youtube.com/watch?v=Fy9dJgGCWZI

## Slide 32: Answer: Exercise 2.4
Write the procedures for generating a spectrogram from a source signal X.
Answer: to be completed by students